## Slide 1: Particle Photon Sparkfun Weather Shield and Microsoft Azure

## Slide 2: HANDS-ON-LAB WALKTHROUGH
http://aka.ms/pwshol
Go ahead and open it, but we’ll walk through it here.

## Slide 3: Installing prerequisites

## Slide 4: Create a free particle.io account
Go to http://particle.io
Click on the “build” link: http://build.particle.io/build
Create an account (free)

## Slide 5: Install prerequisites
Install Node 0.12.4 (Yes, and older version) https://nodejs.org/download/release/v0.12.4/ Need a version manager for node? Check out https://github.com/creationix/nvm for Mac OSx or Linux or http://github.com/coreybutler/nvm-windows for Windows
Download and install Python 2.x (not 3+) https://www.python.org/downloads/
On Windows? You need Visual Studio C++ tools: http://aka.ms/msbuild2013
REBOOT AFTER

## Slide 6: Windows C++ tools requirement
Already have VS installed, but not the C++ tools?
  From “Control Panel” | “Programs” modify your VS install:

## Slide 7: Windows C++ tools requirement
Don’t have Visual Studio installed?
  Install MSBuild for VS2013: http://aka.ms/msbuild2013

## Slide 8: Install the particle-cli
npm install particle-cli -g
If it doesn’t build right on Windows, try adding:
npm install particle-cli –g --msvs_version=2013

## Slide 9: Login to the particle-cli
From a command prompt: particle login
Use the credentials for the particle account you created previously.

## Slide 10: Setting up and claiming the photon

## Slide 11: Connect the photon to your computer via usb cable
On Windows? Install the driver: http://aka.ms/photondriver
Extract the .zip file to a folder on your computer:
Open Device Manager
Right click-on the un-recognized device
Select “Update Driver Software…”
Point to the folder where you extracted the driver
Complete the install
Note the COM port it is attached to

## Slide 12: Identify the attached photon
First find the COM port it is attached to: particle serial list
Then, get the device ID: particle serial identify
Copy the Photon ID to your clipboard and save somewhere for later

## Slide 13: Configure the particle wifi
From the command prompt: particle serial wifi Follow the prompts to connect the WiFi: <your wifi ssid> <your wifi security mode> <your wifi cypher type> <your wifi password>

## Slide 14: Claim and name your photon
Then, get the device ID, copy the reported ID to your clipboard (Make sure the Photon is in Listening Mode ): particle serial identify
Add the device to your account particle device add <id>
Name the device particle device rename <id> <newname>

## Slide 15: Creating the webhook

## Slide 16: Download the webhook.json
http://aka.ms/pwsholwebhook
Save it to a known folder on your computer
Open the webhook.json file to review it
YOU DO NOT NEED TO MAKE ANY CHANGES AT THIS POINT
Learn more about Particle Webhooks here: http://aka.ms/pwh

## Slide 17
{
"event": "ConnectTheDots",
"url": "https://connectthedotsex-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "mBLQGWxSkRHg7f2eRCLonHUpNS+DY0iPHclxjf7Cmvk="
},
"mydevices": true
}

## Slide 18
{
"event": "ConnectTheDots",
"url": "https://connectthedotsex-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "mBLQGWxSkRHg7f2eRCLonHUpNS+DY0iPHclxjf7Cmvk="
},
"mydevices": true
}
The name of the “event” that will invoke the webhook.
When you call Spark.publish("ConnectTheDots", payload); from your Photon, the Particle cloud back end will trigger this webhook and publish your payload to the Azure Event Hub, specified by the “url”

## Slide 19
{
"event": "ConnectTheDots",
"url": "https://connectthedotsex-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "mBLQGWxSkRHg7f2eRCLonHUpNS+DY0iPHclxjf7Cmvk="
},
"mydevices": true
}
The “url” of the Azure Event Hub that the data will be published to.
In this case, we are posting to the “connectthedotsex-ns” service bus namespace into an event hub named “ehdevices”

## Slide 20
{
"event": "ConnectTheDots",
"url": "https://connectthedotsex-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "mBLQGWxSkRHg7f2eRCLonHUpNS+DY0iPHclxjf7Cmvk="
},
"mydevices": true
}
The data will be sent to the url using an HTTP POST

## Slide 21
{
"event": "ConnectTheDots",
"url": "https://connectthedotsex-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "mBLQGWxSkRHg7f2eRCLonHUpNS+DY0iPHclxjf7Cmvk="
},
"mydevices": true
}
The json template is used to create the data for the message that will be sent to the Azure Event Hub

## Slide 22
{
"event": "ConnectTheDots",
"url": "https://connectthedotsex-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "mBLQGWxSkRHg7f2eRCLonHUpNS+DY0iPHclxjf7Cmvk="
},
"mydevices": true
}
{
“s”: ”wthr”,
“u”: “F”,
“m”: “Temperature”,
“v”: 79.234,
“o”: “WearHacks LA”,
“d”: “Brets Demo Photon” “l”: “LA”,
} Sample Payload from the Photon’s Spark.Publish call

## Slide 23
{
"event": "ConnectTheDots",
"url": "https://connectthedotsex-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "mBLQGWxSkRHg7f2eRCLonHUpNS+DY0iPHclxjf7Cmvk="
},
"mydevices": true
}
The values:
SPARK_PUBLISHED_AT and SPARK_CORE_ID
Are supplied by the Particle cloud back end

## Slide 24
{
"event": "ConnectTheDots",
"url": "https://connectthedotsex-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "mBLQGWxSkRHg7f2eRCLonHUpNS+DY0iPHclxjf7Cmvk="
},
"mydevices": true
}
The Shared-Access-Signature key name, and key value used to access the Azure Event Hub

## Slide 25
{
"event": "ConnectTheDots",
"url": "https://connectthedotsex-ns.servicebus.windows.net/ehdevices/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "D1",
"key": "mBLQGWxSkRHg7f2eRCLonHUpNS+DY0iPHclxjf7Cmvk="
},
"mydevices": true
}
Restricts the webhook to being triggered only from events published from your own devices

## Slide 26: Create the particle webhook
From the command prompt, get in the same folder as the webhook.json file you downloaded, and run: particle webhook create webhook.json
Other particle-cli webhook commands include: particle webhook list particle webhook delete hookid

## Slide 27: Programming the photon

## Slide 28: Assemble the photon and weather shield

## Slide 29: Create the particleweathershield Sketch
Create a new “App” here: https://build.particle.io/build/new
Name it “ParticleWeatherShield”
Download the sketch from: http://aka.ms/pwsholsketch
Copy the text from the downloaded ParticleWeatherShield.ino file
Paste into the ParticleWeatherShield app in Particle Build

## Slide 30: Add the Weather Shield library
In the Particle Build web interface, click the “Libraries” icon
Search for the SparkFun_Photon_Weather_Shield_Library
Select it, and then click the “INCLUDE IN APP” button:
Then, select the “ParticleWeatherShield” app, and click the “ADD TO THIS APP” button

## Slide 31: Library include and fields
// This #include statement was automatically added by the Particle IDE.
#include "SparkFun_Photon_Weather_Shield_Library/SparkFun_Photon_Weather_Shield_Library.h"
Weather sensor;
char Org[] = "WearHacks LA";
char Disp[] = "Brets Demo Photon";
char Locn[] = "LA";

## Slide 32: Setup method
void setup()
{
Serial.begin(9600);
sensor.begin();
sensor.setModeBarometer();//Set to Barometer Mode
sensor.setOversampleRate(7); // Set Oversample rate
sensor.enableEventFlags(); //Necessary register calls to enble temp, baro ansd alt
}

## Slide 33: Loop method, and sensor reading
void loop()
{
// Measure Relative Humidity from the HTU21D or Si7021
float humidity = sensor.getRH();
// Measure Temperature from the HTU21D or Si7021
float tempf = sensor.getTempF();

## Slide 34: Publish temperature data
delay(5000);
char payload[255];
snprintf(payload, sizeof(payload), "{
\"s\":\"wthr\",
\"u\":\"F\",
\"l\":\"%s\",
\"m\":\"Temperature\",
\"o\":\"%s\",
\"v\": %f,
\"d\":\"%s\" }", Locn, Org, tempf, Disp);
Spark.publish("ConnectTheDots", payload);
Serial.println(payload);
{
“s”: ”wthr”,
“u”: “F”,
“l”: “LA”,
“m”: “Temperature”,
“o”: “WearHacks LA”,
“v”: 79.234,
“d”: “Brets Demo Photon” }
Sample Payload

## Slide 35: Publish humidity data, end loop
delay(5000);
snprintf(payload, sizeof(payload),
"{ \"s\":\"wthr\",
\"u\":\"%%\",
\"l\":\"%s\",
\"m\":\"Humidity\",
\"o\":\"%s\",
\"v\": %f,
\"d\":\"%s\" }", Locn, Org, humidity, Disp);
Spark.publish("ConnectTheDots", payload);
Serial.println(payload);
}
{
“s”: ”wthr”,
“u”: “%”,
“l”: “LA”,
“m”: “Humidity”,
“o”: “WearHacks LA”,
“v”: 33,
“d”: “Brets Demo Photon” }
Sample Payload

## Slide 36: Modify the metadata properties
Put your own values in. Make sure that the “Display Name” is appropriate and identifies your Photon clearly: char Org[] = "ORGANIZATION_NAME"; char Disp[] = "DISPLAY_NAME"; char Locn[] = "LOCATION";

## Slide 37: Save, verify and flash
Click the save icon to save your sketch:
Click the verify icon to compile and verify:
Click the flash icon to deploy your sketch:

## Slide 38: Monitoring your photon

## Slide 39: Monitor your photon
From the command prompt, to monitor all events or just a single event: particle subscribe mine or particle subscribe {webhook event name, eg “ConnectTheDots”}
To monitor the Serial output from a photon attached to your pc: particle serial monitor <COMPORT>
To see events in the particle.io dashboard, go to: https://dashboard.particle.io/user/logs
To see the data values coming in to the pre-made “ConnectTheDots” site: http://aka.ms/pwsholweb

## Slide 40: http://aka.ms/pwsholweb
Click device names along the left to show or hide them in the graphs

## Slide 41: Where to go from here?
Publish other sensor values
Create your OWN event hubs and consume the data you publish
  Create an Azure Subscription using the Free Trial, or see me for an Azure Pass
  Create your own Event Hubs in Azure: http://aka.ms/ctdazureprep
  Create your own ConnectTheDots dashboard web site: http://aka.ms/ctdazuresite
  Learn about other ways to consume the data from the ConnectTheDots samples: http://connectthedots.io

## Slide 42: resources:
This deck, and other event resources: http://aka.ms/whla
Info about Particle and Azure: https://www.particle.io/microsoft
Azure Documentation http://azure.microsoft.com
Azure Portal https://manage.windowsazure.com and https://portal.azure.com
Particle Documentation http://docs.particle.io

## Slide 43: IoT Logo

## Slide 44: arduino

## Slide 45: GALILEO BOARD

## Slide 46: LEDs

## Slide 47: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 48: cables

## Slide 51: Micro SD Cards
Font: Segoe UI Semibold